## Slide 1: CREST 持続可能な水利用を実現する革新的な技術とシステム 安全で持続可能な水利用のための放射性物質移流拡散シミュレータの開発 あ
東京大学 大気海洋研究所
芳村圭
大気拡散シミュレーション分野
現状についての報告@2012/8/27

## Slide 2: Updates
Dr. Eun-Chul Chang joined our team.
  Appointed for implementation of semi-lagrangian transport for tracers.
Realistic emission has been implemented.
Sensitivity of three parameters was examined.
  Wet deposition rate
  Dry deposition rate
  Horizontal diffusivity
Make the code transferable. (Eun-Chul and Saya have already started their calculations.)

## Slide 3: Radioactive Tracer Experiments with IsoRSM
Model:
  IsoRSM (Yoshimura et al., 2010)
Lateral Boundary Condition
  NCEP-R2 with Spectral Nudging
Domain/Resolution
  161x200/10km Mercator
  Lon: 132.7E to 151.5E
  Lat: 28.3N to 46.7N
Period
  2011/03/12 0Z – 3/28 0Z
Physical Processes
  RAS convective precipitation
  Non-Local K PBL
Tracer type / Emission
  131I and 137Cs
  Emitted at 140.9E/37.34N with Chino et al. (2011)
Deposition processes
  Next pages

## Slide 4: Wet Deposition
The equation commonly used:
  In Brenk and Vogt, 1982:A=0.18, B=0.8
  In Maryon, 1992: A=0.55, B=0.79 for rainout A=0.14, B=0.79 for washout
In our study:
  Proportional to condensation amount P and anti-proportional to vapor amount q. When the tracer is preferably included into condensed water, α>1.
  With the previous equation, wet deposition (scavenging) occurs too little due to small condensation P at very low temperature area/height.

## Slide 5: Dry Deposition
Fdry: dry deposition fallout (Bq/m2/s), Vd: deposition velocity (m/s), C(z=1): Concentration at the model’s lowest layer (Bq/m3)
  Vd=1e-3 on sea, 5e-3 on land for Cs137
  Vd=5e-3 on sea, 25e-3 on land for I131
Based on Maryon et al. (1992)

## Slide 6: Horizontal Diffusion
yi: Spectral coefficient (prognostic variable)
βi: Damping rate
Dc: Diffusivity coefficient
β

## Slide 7: Parameters of Control Experiment
 |  | I131 | Cs137
α (ND) |  | 1 | 1
Vd (m/s) | Land | 25e-3 | 5e-3
 | Sea | 5e-3 | 1e-3
Dc (ND) |  | 0.2 | 0.2

## Slide 8: I131 Emission and Deposition
All Domain

## Slide 9: Cs137 Emission and Deposition

## Slide 11: Comparison with similar effort (3/12)

## Slide 12: Comparison with similar effort (3/14)

## Slide 13: Comparison with similar effort (3/15)

## Slide 14: Comparison with similar effort (3/20)

## Slide 15: Comparison with similar effort (3/21)

## Slide 16: Comparison with similar effort (3/22)

## Slide 17: Cs137 Total Deposition in Mar2011

## Slide 18: With other models
Our study | 17 | 33 | 50
Deposition Rate (%)
Land
Sea
OB

## Slide 19: Sensitivity Experiments
Cs137 | E | WD_tot | WD_land | WD_sea | Atm | DD_tot | DD_sea | TD_tot | TD_land | TD_sea
S24 α=1 Vd=1e-3 Dc=0.2 | 8.56 | 2.72 | 0.27 | 2.45 | 0.53 | 1.56 | 0.40 | 4.28 | 1.43 | 2.85
 | 100.00% | 31.81% | 3.21% | 28.60% | 6.16% | 18.20% | 4.65% | 50.01% | 16.76% | 33.25%
S25 α=1 Vd=1e-3 Dc=2 | 8.56 | 2.84 | 0.24 | 2.60 | 0.49 | 1.73 | 0.38 | 4.57 | 1.59 | 2.98
 | 100.00% | 33.19% | 2.77% | 30.42% | 5.71% | 20.23% | 4.39% | 53.42% | 18.61% | 34.81%
S26 α=1.5 Vd=0.2e-3 Dc=2 | 8.56 | 4.23 | 0.36 | 3.87 | 0.53 | 0.40 | 0.08 | 4.63 | 0.68 | 3.95
 | 100.00% | 49.44% | 4.22% | 45.22% | 6.23% | 4.67% | 0.98% | 54.11% | 7.91% | 46.20%
I131 | E | WD_tot | WD_land | WD_sea | Atm | DD_tot | DD_sea | TD_tot | TD_land | TD_sea
S24 α=1 Vd=5e-3 Dc=0.2 | 147.74 | 28.38 | 2.61 | 25.77 | 7.08 | 71.94 | 25.28 | 100.32 | 49.28 | 51.05
 | 100.00% | 19.21% | 1.77% | 17.44% | 4.79% | 48.69% | 17.11% | 67.90% | 33.35% | 34.55%
S25 α=1 Vd=5e-3 Dc=2 | 147.7 | 26.9 | 2.1 | 24.8 | 6.5 | 75.4 | 23.7 | 102.3 | 53.8 | 48.5
 | 100.00% | 18.21% | 1.42% | 16.79% | 4.40% | 51.04% | 16.03% | 69.25% | 36.43% | 32.81%
S26 α=1.5 Vd=1e-3 Dc=2 | 147.7 | 55.4 | 4.2 | 51.3 | 9.2 | 24.0 | 6.9 | 79.5 | 21.2 | 58.2
 | 100.00% | 37.53% | 2.83% | 34.70% | 6.24% | 16.25% | 4.70% | 53.78% | 14.38% | 39.40%
Control
Less Diffusive
More wet/ Less Dry Dep.
Control
Less Diffusive
More wet/ Less Dry Dep.

## Slide 20: Sensitivity Experiments (Deposition Distribution)
Control
Less Diffusive
Less Diffusive + More Wet/Less Dry dep.

## Slide 21: Concerns
Too strong diffusivity compared to the real.
Less land deposition compared to other models.
Too little (too large) wet (dry) deposition?

## Slide 22: Todo
More accurate dynamics
  Semi-lagrangian transport (Eun-Chul)
  Sensitivity Experiments (A. Saya)
  Non-hydrostatic behavior (prognostic vertical motion)
More sensitivity experiments.
  The three Parameters.
  Lateral BC (NCEP2, JRA25, ERA-I)
  Initial BC (starting from 3/10, 11, 12, etc.)
  Emission (Chino et al., Stohl et al., etc.)
  Domain size
Imaginary situations
  Ooi NP in Fukui
  “What if”s (e.g., what if the Earthquake occurred on 10 Mar?)

## Slide 23: 他機関大気拡散解析
131I : 5×10-3 m/s
137Cs : 1×10-3 m/s
JAEA
国環研
JAMSTEC
電中研
機関